## Slide 1: Bule Hora University
Department of Electrical and Computer Engineering
Assignment for Electromagnetic field(EMF)
Group1 Members:
Name ID
1.lamessa mosisa..................0274/16
2.Robika Daba.......................0173/16
3.Gezu Diriba.........................0411/16
4.Ifa Garoma..........................0050/16
5.Ebiso Bati.............................0273/16
6.Nafyad Bayisa......................0171/16
7.Gelana motii........................0154/16
College of Engineering and Technology

## Slide 2: Faraday’s Laws of Electromagnetic induction
Faraday’s law explains how a changing magnetic field induces an electromotive force (EMF) in a closed loop.
A time-varying magnetic flux through any surface produces a circulating electric field around its boundary.
This phenomenon forms the basis of generators, transformers, and inductive systems.
Integral form relates induced EMF to rate of change of magnetic flux.

## Slide 3: Point Form and (Faraday’s Law)
Differential form: curl of E = negative rate of change of B.
Electric field results from magnetic field changes, not charge separation.
Stokes’ theorem converts line integral to surface integral.
If integral holds for all surfaces, it must hold at every point.

## Slide 4: Maxwell’s Fourth Equation (Curl E = – dB/dt)
This is the differential form of Faraday’s law.
A time-varying magnetic field generates a circulating electric field.
Induced electric field forms closed loops, not from electric charges.
Fundamental for understanding electromagnetic wave generation.

## Slide 5: Point Relationship & (Maxwell’s Equation)
Gives point-by-point relationship between changing B-fields and E-fields.
A curling electric field appears where magnetic field varies with time.
Derivation uses Stokes’ theorem to convert loop integral to surface integral.
Maxwell used this to unify electric & magnetic behavior.

## Slide 6: Statically and Dynamically Induced EMF
Induced EMF can occur in two ways.
Static (Motional) EMF: conductor moves in constant magnetic field.
Magnetic force separates charges → EMF.
Depends on velocity, field strength, orientation.
Used in generators and rotating machines.

## Slide 7: Dynamic EMF & Applications
Dynamic EMF occurs even if conductor is stationary.
Arises from time-varying magnetic field linking conductor.
Based on Faraday’s law.
Applications: transformers, electrical machines, induction systems.
Parameters: field strength, conductor length, loop radius, flux rate.

## Slide 8: mathimathical derivation and example
Magnetic force on a charge:
Derivetion
Work done to move a charge along
the conductor:
Induced EMF:
Example:
1. A 0.5 m long conductor moves at 2 m/s perpendicular to a magnetic field of 0.3 T. Find the induced EMF.
Solution:
✅ Answer: EMF = 0.3 V

## Slide 9: Modification of Maxwell’s Equations
Maxwell added displacement current to Ampère’s law.
Completed four Maxwell equations.
Describes fields when changing with time.
Ensures correct predictions in capacitors.
Foundation of EM wave propagation.

## Slide 10: Importance of Maxwell’s Modification
Without displacement current → incorrect magnetic field prediction.
Ensures charge continuity.
Unifies electric & magnetic phenomena.
Leads to discovery of electromagnetic waves.

## Slide 11: Time-Harmonic Fields
Time-harmonic fields vary sinusoidally (AC systems, EM waves).
Represent steady-state behavior.
Use phasors → simplified analysis.
Phasors convert differential equations to algebraic form.

## Slide 12: Frequency-Domain Representation
Fields expressed using sinusoidal functions with angular frequency.
Maxwell equations take compact phasor forms.
Describe E and B relationships at fixed frequency.
Essential for AC circuits, wave propagation, resonance.

## Slide 13: Thank You !!!